1st midterm exam ANTENNAS AND PROPAGATION - 18.10.2016

1. If we see suspicious signals on a spectrum analyzer, that may not really exist, but are just a nonlinear product inside the spectrum analyzer, the countermeasure is:

(A) narrow	(B) increase	(C) increase the	(D) narrow the
the resolution	the sweep time	input attenuation	video filter

2. The 3D spherical coordinate system (r,Θ,Φ) is right-handed with the north pole in the direction of the Cartesian axis z. Converting the spherical coordinates (r,Θ,Φ) into Cartesian coordinates (x,y,z) the Cartesian coordinate x is obtained as:

(A) r.sinΘ.sinΦ	(B) r.sinΘ.cosΦ	(C) r.cosΘ.sinΦ	(D) r.cosΘ.cosΦ

3. A hollow metal pipe of circular cross-section is used as a waveguide on its fundamental mode. The forward wave has the following electric field E components:

(A) only	(B) only	(C) both transversal	(D) does not
transversal E	longitudinal E	and longitudinal E	have any E

4. The vector potential A is computed from the current density J by solving the vector wave equation ΔA+ω2μεA=-μJ. The wave equation for the vector potential (as written here) works with the following units (MKSA):

(A) Vs	(B) Vs/m	(C)	Vs/m2	(D) Vs/m3

5. The largest radio-telescope on the world was built in China with the diameter of the primary mirror equal to d=500m. At what distance r=? starts its far field while operating at the hydrogen-line frequency of 1.42GHz? (c0≈3•108m/s)

(A) 4733m	(B) 211km	(C) 2367km	(D) 11200km

6. A switching power supply includes a transformer causing radio interference at a frequency of f=50kHz. At what distance r=? are its electric field E and magnetic field H approximately in the ratio of the free-space wave impedance Z0≈377Ω? (c0≈3•108m/s)

(A) 9.55cm	(B) 9.55m	(C) 95.5m	(D) 955m

7. The radiation pattern of a ground-plane antenna at f=180MHz is being spoiled by unwanted currents in the supporting mast. The length l=? of the radials (rods forming the skirt of the antenna) is chosen for the lowest mast current: (c0≈3•108m/s)

(A) 0.4m	(B) 0.5m	(C) 0.6m	(D) 0.7m

8. A street light contains a P=250W bulb with an efficiency of η=30% on a h=7m high pole above ground. What is power-flux density of light |S|=? on the ground at a horizontal distance x=5m from the pole? The atmospheric attenuation can be neglected.

(A) 81mW/m2	(B) 364mW/m2	(C) 3.64W/m2	(D) 81W/m2

9. GPS navigation satellites are circling the Earth at an altitude of h=20200km above the surface. What directivity D=? is required for the on-board antenna to cover the whole visible hemisphere? The Earth is assumed a sphere with a diameter of R=6378km.

(A) 12.4dBi	(B) 15.4dBi	(C) 18.4dBi	(D) 24.4dBi

10. The gain G is measured in a free-space link between two identical unknown antennas at a distance of r=3m. What is the expected uncertainty ΔG [dBi] of the measurement due to the uncertainty of each antenna phase center amounting to Δr=+/-10cm?

(A) +/-0.1dBi	(B) +/-0.6dBi	(C) +/-1.5dBi	(D) +/-4dBi

11. A weather satellite is transmitting on f=137.5MHz with a power of PTX=5W to an omnidirectional antenna GTX=1. What is the maximum radio range r=? to a ground station with an omnidirectional antenna GRX=1 and receiver sensitivity PRX=-110dBm? (c0≈3•108m/s)

(A) 487km	(B) 974km	(C) 1948km	(D) 3897km

12. A fluorescent light bulb is causing interference to a medium-wave receiver (λ=300m) with its electric field Ei. The best countermeasure against this interference is:

(A) a ferrite	(B) an electrical	(C) reorienting the	(D) there is no
receiving antenna	whip antenna	receiving antenna	countermeasure

Name:	Email: