3rd midterm exam ANTENNAS AND PROPAGATION - 6.12.2016

1. A vector voltmeter is used as a conventional voltmeter to measure the amplitude of a single signal. The phase is not measured. The unknown signal should be connected:

(A) exclusively	(B) the same to	(C) exclusively	(D) measurement
    to input A	input A or B	to input B	impossible

2. A broad-side array includes two half-wave dipoles oriented in the same way and polarized in the same way. The measurement of the two-port impedance matrix of the two dipoles shows |Z11|≈|Z22|>>|Z21|≈|Z12|. The distance h between the two dipoles is:

(A) h=λ/2	(B) h>>λ/2	(C) h=λ/4	(D) h<<λ/4

3. A corrugated horn is excited by a circular waveguide at a frequency supporting the fundamental TE11 mode only. The waveguide electric field E has the following components in cylindrical coordinates (ρ,φ,z) with the Z axis corresponding to the waveguide axis:

(A) E=1φEφ+1zEz	(B) E=1φEφ	(C) E=1ρEρ+1φEφ	(D) E=1ρEρ

4. A broad-side array includes two identical, commercial antennas for f=144MHz. The only available information are the -3dB main-lobe beam widths of αE=30º and αH=40º.
What should be the stacking distance h=? in the H plane? (c0=3•108m/s)

(A) 1.04m	(B) 1.52m	(C) 2.08m	(D) 3.05m

5. An end-fire array spaced at h=3/4λ in the Z axis includes two half-wave dipoles both oriented in the X axis. The dipoles are fed in quadrature I2=jI1, meaning a one-quarter period phase shift. How many lobes has the resulting radiation pattern?

(A) 3	(B) 4	(C) 2	(D) 5

6. The measured amplitude radiation pattern of an unknown antenna is equal to F(θ,Φ)=√1-sin2θ∙sin2Φ. What kind of antenna is it and how is it oriented?

(A) λ/2 dipole	(B) small loop	(C) Huygens source	(D) short wire
in the X axis	in the YZ plane	in the XZ plane	in the Y axis

7. Measuring the gain of an antenna by receiving the mirror image of the same antenna, a signal source producing the following radio signal is used:

(A) unmodulated	(B) AM ON/OFF	(C) AM ON/OFF	(D) FM 1MHz
    carrier (CW)	1kHz	27.8kHz	wide deviation

8. The transmitting antenna has the ratio of circularly-polarized components QO=j0.333. What is the required polarization of the receiving antenna QS=? to get the strongest reception? The gain of the receiving antenna is constant. (j=√-1)

(A) -j3	(B) j3	(C) -j0.333	(D) j0.333

9. A right-hand circularly-polarized antenna includes two identical linearly-polarized Yagi antennas. Each has a gain of G=12dBi. The quadrature and impedance matching network has a=-0.3dB insertion loss. What is the gain of the overall antenna GRHCP=?

(A) 9.3dBi	(B) 11.7dBi	(C) 14.7dBi	(D) 15.3dBi

10. The omnidirectional antenna of a portable radio achieves a noise temperature of TA=400K at f=162MHz. The noise temperature of the receiver is TS=600K. What is the minimum signal power PMIN=? for a S/N=10dB in a bandwidth B=15kHz? (kB=1.38•10-23J/K)

(A) 8.3•10-16W	(B) 8.3•10-14W	(C) 2.07•10-16W	(D) 2.07•10-15W

11. Pointing a loss-less antenna with a directivity of D=17dBi (ΩA>>ΩS) to the Sun (angular diameter αS=0.5º), its noise temperature rises by ΔTA=300K compared to the cold sky. What is the black-body temperature T=? of the Sun at this frequency?

(A) 1.26•106K	(B) 1.003•105K	(C) 5.96•103K	(D) 1.58•107K

12. A parabolic-mirror antenna is pointed to the Sun. Its noise temperature increases by ΔTA=1000K with a linearly-polarized feed. What is the temperature increase ΔTA'=? with a circularly-polarized feed, if the efficiency of both feeds is identical?

(A) 500K	(B) 1000K	(C) 1414K	(D) 2000K

Name:	Email: