1. tiha vaja iz VISOKOFREKVENČNE TEHNIKE - 21.10.2016

1. Hitrost delovanja polprevodniških gradnikov je ključno odvisna od mobilnosti nosilcev naboja [cm2/Vs]. Mobilnost elektronov označimo z μn, mobilnost vrzeli pa z μp.
Sodobni tranzistorji za visoke frekvence so iz polprevodnika GaN, za katerega velja:

(A) μn<<μp	(B) μn=μp	(A) μn=0	(D) μn>>μp

2. Dioda 1N4007 je počasna usmerniška PN dioda, dioda 1N5818 pa guard-ring Schottky.
Obe sta v enakem ohišju in za obe velja enačba diode I=IS.(exp(U/nUT)-1). Diodi se razlikujeta v naslednjih električnih lastnostih (obkrožite NAPAČEN odgovor):

(A) IS_Schottky>>IS_PN	(B) trr_Schottky<<trr_PN	(C) UT_Schottky>UT_PN	(D) nSchottky<nPN

3. Barvo svetleče diode v glavnem določa širina prepovedanega energijskega pasu polprevodnika. Zeleno svetlečo diodo običajno izdelamo kot PN spoj iz naslednjega polprevodnika:

(A) GaP	(B) InP	(C) GaN	(D) GaAs

4. PIN dioda ima ob pritisnjeni zaporni napetosti kapacitivnost 0.3pF. Kolikokrat se poveča kapacitivnost PIN diode, ko skozi teče tok I=3mA v prevodni smeri? Življenjska doba nosilcev naboja je τ=100ns. V enačbi diode I=IS.(exp(U/nUT)-1) je n≈2 in UT≈26mV.

(A) 200-krat	(B) 20000-krat	(C) 20-krat	(D) 2000-krat

5. Gunn-ov element ali Transferred-Electron Device (ime dioda ni najbolj primerno) pogosto uporabljamo kot negativno upornost v mikrovalovnih oscilatorjih. Gunn-ov element lahko izdelamo iz naslednjega polprevodnika s primernimi energijskimi pasovi:

(A) GaAs	(B) Si	(C) PbS	(D) SiGe

6. Tokovno ojačanje bipolarnega tranzistorja v vezavi s skupno bazo zapišemo α=IK/IE. Tokovno ojačanje istega tranzistorja v vezavi s skupnim emitorjem zapišemo β=IK/IB. Parametra α in β sta med sabo povezana na naslednji način (IE=IB+IK):

(A) β=1-α	(B) β=α/(1-α)	(C) β=(1-α)/α	(D) β=α+1

7. Ojačevalnik z bipolarnimi tranzistorji ima izhodno stopnjo v razredu B v mirujočem stanju. Ko ojačevalnik krmilimo do nazivne izhodne moči, se povprečna poraba (povprečni tok) izhodne stopnje:

(A) zmanjša	(B) ostane enak	(C) poveča	(D) gre na nič

8. Silicijev NPN tranzistor ima mejno frekvenco fT=2GHz v vezavi s skupnim emitorjem. Isti tranzistor dosega tokovno ojačanje β0=150 pri zelo nizkih frekvencah. Kolikšno je tokovno ojačanje tranzistorja β=? pri frekvenci f=100MHz?

(A) 150	(B) 5	(C) 50	(D) 20

9. Sekundarni preboj je najbolj verjeten v silicijevem bipolarnem tranzistorju pod naslednjimi pogoji, v vseh primerih ob enaki moči na čipu P=konst.:

(A) visoka VF	(B) visoka DC	(C) velik RF	(D) velik DC
    napetost	napetost	tok	tok

10. MOSFET iz silicija ima štiri neodvisne elektrode: vrata G, izvor S, podlago B in ponor D. Silicijev MOSFET je običajno vgrajen v ohišje s tremi električni priključki. Pri tem sta običajno spojeni skupaj dve elektrodi na isti priključek:

(A) S+B	(B) G+B	(C) G+S	(D) D+B

11. N-kanalni MOSFET z induciranim kanalom ima pragovno napetost UTH=+3V. Pri napetosti vrat UGS=+4V doseže tok ponora ID=1A pri napetosti UDS=+10V. Kolikšen je pričakovani tok ponora ID'=? pri UGS'=5.5V in isti UDS?

(A) 1.25A	(B) 2.50A	(C) 6.25A	(D) 8.75A

12. GaAlAs/GaAs HEMT z vgrajenim kanalom je odličen visokofrekvenčni ojačevalnik. Pri uporabi moramo paziti, da skozi vrata ne steče prevelik tok in ne poškoduje kanala. Katere od navedenih napetosti UGS NE smemo priključiti na vrata HEMT?

(A) -1.5V	(B) -0.3V	(C) +0.3V	(D) +1.5V

Priimek in ime:	Elektronski naslov:
1st midterm exam HIGH-FREQUENCY TECHNOLOGY - 21.10.2016

1. The operating speed of semiconductor devices critically depends on the charge-carrier mobility [cm2/Vs]. Let μn denote the electron mobility and μp. denote the hole mobility. Modern high-frequency transistors are made of GaN, where the following holds:

(A) μn<<μp	(B) μn=μp	(A) μn=0	(D) μn>>μp

2. The diode 1N4007 is a slow PN rectifier while the 1N5818 is a guard-ring Schottky. Both come in the same package and the diode equation I=IS.(exp(U/nUT)-1) holds for both. The diodes differ in the following properties (circle the WRONG answer):

(A) IS_Schottky>>IS_PN	(B) trr_Schottky<<trr_PN	(C) UT_Schottky>UT_PN	(D) nSchottky<nPN

3. The color of a light-emitting diode is mainly defined by the energy bandgap of the semiconductor material. A green light-emitting diode is usually manufactured as a PN junction from the following material:

(A) GaP	(B) InP	(C) GaN	(D) GaAs

4. At reverse bias, a PIN diode has a capacitance of 0.3pF. How many times the capacitance increases at a forward current of I=3mA? The minority-carrier lifetime is τ=100ns. In the diode equation I=IS.(exp(U/nUT)-1) the constants are n≈2 and UT≈26mV.

(A) 200-times	(B) 20000-times	(C) 20-times	(D) 2000-times

5. A Gunn element or Transferred-Electron Device (the name diode is not appropriate) is frequently used as a negative resistance in microwave oscillators. A Gunn element can be manufactured from the following semiconductor with appropriate energy bands:

(A) GaAs	(B) Si	(C) PbS	(D) SiGe

6. The current gain of a bipolar transistor in a common-base configuration is α=IK/IE. The current gain of the same transistor in a common-emitter configuration is β=IK/IB. The parameters α and β are related in the following way (IE=IB+IK):

(A) β=1-α	(B) β=α/(1-α)	(C) β=(1-α)/α	(D) β=α+1

7. A bipolar-transistor amplifier has the output stage biased for class B operation in the quiescent state. When the amplifier is driven to produce its rated output power, the average current drain of its output stage:

(A) decreases	(B) stays the same	(C) increases	(D) goes to zero

8. A silicon NPN transistor has its common-emitter transition frequency fT=2GHz. At very low frequencies its current gain rises up to β0=150. What is the transistor current gain β=? at a frequency of f=100MHz?

(A) 150	(B) 5	(C) 50	(D) 20

9. A secondary breakdown is most likely to happen in a silicon bipolar transistor under the following conditions, all of them at the same dissipated power P=const.:

(A) high RF	(B) high DC	(C) high RF	(D) high DC
    voltage	voltage	current	current

10. A silicon MOSFET has four independent electrodes: gate G, source S, drain D and substrate B (Bulk). A silicon MOSFET is usually available in a package with three terminals only. The following two electrodes are connected to a single terminal:

(A) S+B	(B) G+B	(C) G+S	(D) D+B

11. A N-channel enhancement MOSFET has a gate threshold voltage UTH=+3V. At a gate voltage UGS=+4V, the drain current reaches ID=1A at an UDS=+10V. What is the expected drain current ID'=? at UGS'=5.5V and same UDS?

(A) 1.25A	(B) 2.50A	(C) 6.25A	(D) 8.75A

12. A depletion-mode GaAlAs/GaAs HEMT is an excellent high-frequency amplifier. The gate current should be limited to avoid damaging the channel. Which gate voltage UGS should NOT be applied to the gate of the HEMT?

(A) -1.5V	(B) -0.3V	(C) +0.3V	(D) +1.5V

Name:	Email: