3rd midterm exam HIGH-FREQUENCY TECHNOLOGY - 2.12.2016

1. A thermal RF power meter requires zero calibration of its thermocouple for any measurement to be valid. Erroneously the power meter is zeroed to an input power of Po=100μW. What is the indicated power P'=? when we connect it to a source P=300μW?

(A) 100μW	(B) 200μW	(C) 300μW	(D) 400μW

2. What noise temperature TS=? can be achieved in a low-noise amplifier with a GaAlAs/GaAs HEMT at a frequency of f=3GHz? The whole amplifier is cooled with liquid nitrogen to TLN2=77K and impedance matching for optimum noise is used.

(A) 1000K	(B) 100K	(C) 10K	(D) 1K

3. A silicon-diode chip is installed in a Mini-MELF SMD package. The latter carries a single color ring. The meaning of this ring is the following:

(A) anode	(B) breakdown	(C) capacitance	(D) cathode
connection	voltage	tolerance	connection

4. A broadband thermal-noise power PN is measured with a spectrum analyzer at a resolution bandwidth B=1MHz and video filter BV=1kHz. What video filter BV'=? is required for a 10-fold decrease of the measurement uncertainty ΔPN?

(A) 10Hz	(B) 100Hz	(C) 300Hz	(D) 10kHz

5. A high-gain GS>>1 satellite receiver is connected to a noise source with an ENR=5dB and cold temperature T1=T0=290K equal to room temperature. The measured hot/cold ratio equals to Y=4dB. What is the noise temperature TS=? of the receiver?

(A) 75K	(B) 125K	(C) 189K	(D) 290K

6. A DVB-T transmitter uses QPSK-OFDM with N=1705 sub-carriers. What is the theoretical peak output power PMAX=? if the transmitter is required to produce an average RF output power <P>=400W?

(A) 235mW	(B) 400W	(C) 16.5kW	(D) 682kW

7. Our transmitter fTX=168MHz is causing interference to our receiver fRX=158MHz only if both are connected through a frequency duplexer to a common antenna on the tower.
What additional transmitters are suspected to cause PIM (passive IMD) on the tower?

(A) 89MHz & 99MHz	(B) 99MHz only	(C) 99MHz & 148MHz	(D) 148MHz only

8. The output stage of a WiFi OFDM transmitter achieves an efficiency of η=3% at an average output power of <P>=200mW. What 1dB compression point P1dB=? is expected if the power amplifier operates in class A?

(A) +13dBm	(B) +23dBm	(C) +33dBm	(D) +43dBm

9. A two-stage amplifier includes three identical building blocks with Ge=10dB and PPI3e=100W. The driver stage uses one building block while the final stage uses two blocks in parallel. What is the overall PIP3=? if the impedance matching is loss-less?

(A) 100W	(B) 167W	(C) 200W	(D) 333W

10. A Doherty power amplifier includes two similar power amplifiers and two quarter-wave delay lines on the input and output. The two power amplifiers differ in their bias, where the Doherty circuit requires operation in the following classes:

(A) A & B	(A) B & dual B	(C) B & C	(D) A & C

11. A microwave isolator includes a circulator with the third port terminated into a matched load. An ideal microwave isolator has the following S parameters:

(A) |S12|=|S21|=1	(B) |S11|=|S22|=1	(B) |S11|=1 &	(B) |S21|=1 &
& S21=S22=0	& S12=S21=0	S12=S21=S22=0	S11=S12=S22=0

12. A frequency band-pass filter includes a single cavity resonator with a loaded QL=300 at a central frequency of f=2GHz. What is the maximum group delay tg=? of such a band-pass filter?

(A) 48ns	(B) 24ns	(C) 12ns	(D) 6ns

Name:	Email: