3. tiha vaja iz VISOKOFREKVENČNE TEHNIKE - 2.12.2016

1. Toplotni merilnik visokofrekvenčne moči zahteva umerjanje ničle termočlena pred veljavno meritvijo moči. Merilnik pomotoma umerjamo, ko je prisotna VF moč Po=100μW. Kolikšno moč P'=? pokaže napačno umerjeni merilnik, ko na vhod pripeljemo P=300μW?

(A) 100μW	(B) 200μW	(C) 300μW	(D) 400μW

2. Kolikšno šumno temperaturo TS=? lahko doseže nizkošumni ojačevalnik z GaAlAs/GaAs HEMTom pri frekvenci f=3GHz? Celotno vezje ojačevalnika hladimo s tekočim dušikom na TLN2=77K in poskrbimo za prilagoditev impedanc za najnižji šum.

(A) 1000K	(B) 100K	(C) 10K	(D) 1K

3. Čip silicijeve diode je vgrajen v Mini-MELF SMD ohišje. Na ohišju je en sam barvni obroček. Pomen barvnega obročka je naslednji:

(A) anodni	(B) prebojna	(C) toleranca	(D) katodni
priključek	napetost	kapacitivnosti	priključek

4. Moč širokopasovnega toplotnega šuma PN merimo s spektralnim analizatorjem pri ločljivosti B=1MHz in video situ BV=1kHz. Katero video sito Bv'=? potrebujemo, da opletanje rezultata ΔPN zmanjšamo za faktor 10-krat?

(A) 10Hz	(B) 100Hz	(C) 300Hz	(D) 10kHz

5. Satelitski sprejemnik z visokim ojačanjem GS>>1 je priključen na šumno glavo z ENR=5dB in hladno temperaturo T1=T0=290K enako sobni temperaturi. Izmerjeno razmerje vroče hladno znaša Y=4dB. Kolikšna je šumna temperatura sprejemnika TS=?

(A) 75K	(B) 125K	(C) 189K	(D) 290K

6. DVB-T oddajnik uporablja QPSK-OFDM z N=1705 podnosilci. Kolikšna je teoretska vršna moč oddajnika PMAX=?, če od oddajnika zahtevamo, da proizvaja povprečno visokofrekvenčno izhodno moč <P>=400W?

(A) 235mW	(B) 400W	(C) 16.5kW	(D) 682kW

7. Naš oddajnik fTX=168MHz moti naš sprejemnik fRX=158MHz samo takrat, ko sta oba povezana preko frekvenčne kretnice na skupno anteno na stolpu. Kateri dodatni oddajniki so potrebni, če sumimo PIM (pasivno intermodulacijsko popačenje) na antenskem stolpu?

(A) 89MHz in 99MHz	(B) samo 99MHz	(C) 99MHz in 148MHz	(D) samo 148MHz

8. Izhodna stopnja WiFi OFDM oddajnika dosega izkoristek η=3% pri povprečni izhodni moči <P>=200mW. Kolikšna je pričakovana moč 1dB nasičenja P1dB=?, če močnostni ojačevalnik deluje v razredu A?

(A) +13dBm	(B) +23dBm	(C) +33dBm	(D) +43dBm

9. Dvostopenjski ojačevalnik vsebuje tri enake gradnike Ge=10dB in PIP3e=100W. V krmilni stopnji uporabimo en gradnik, v izhodni stopnji pa vzporedno vezavo dveh gradnikov. Kolikšna je PIP3=? verige, če prilagoditev impedanc ne vnaša izgub?

(A) 100W	(B) 167W	(C) 200W	(D) 333W

10. Močnostni ojačevalnik v vezavi Doherty vsebuje dva podobna ojačevalnika in dva četrt-valovna zakasnilna voda na vhodu in izhodu. Ojačevalnika se razlikujeta v nastavitvi delovnih točk, kjer vezava Doherty zahteva razreda:

(A) A in B	(A) B in dualni B	(C) B in C	(D) A in C

11. Mikrovalovni izolator vsebuje cirkulator, ki ima tretji priključek zaključen na prilagojeno breme. Idealni mikrovalovni izolator ima naslednje S parametre:

(A) |S12|=|S21|=1	(B) |S11|=|S22|=1	(B) |S11|=1 in	(B) |S21|=1 in
in S21=S22=0	in S12=S21=0	S12=S21=S22=0	S11=S12=S22=0

12. Frekvenčno pasovno-prepustno sito izdelamo z votlinskim rezonatorjem, ki v vezju sita doseže obremenjeni QL=300 pri frekvenci f=2GHz. Kolikšna je največja skupinska zakasnitev tg=? takšnega pasovnega sita?

(A) 48ns	(B) 24ns	(C) 12ns	(D) 6ns

Priimek in ime:	Elektronski naslov:
3rd midterm exam HIGH-FREQUENCY TECHNOLOGY - 2.12.2016

1. A thermal RF power meter requires zero calibration of its thermocouple for any measurement to be valid. Erroneously the power meter is zeroed to an input power of Po=100μW. What is the indicated power P'=? when we connect it to a source P=300μW?

(A) 100μW	(B) 200μW	(C) 300μW	(D) 400μW

2. What noise temperature TS=? can be achieved in a low-noise amplifier with a GaAlAs/GaAs HEMT at a frequency of f=3GHz? The whole amplifier is cooled with liquid nitrogen to TLN2=77K and impedance matching for optimum noise is used.

(A) 1000K	(B) 100K	(C) 10K	(D) 1K

3. A silicon-diode chip is installed in a Mini-MELF SMD package. The latter carries a single color ring. The meaning of this ring is the following:

(A) anode	(B) breakdown	(C) capacitance	(D) cathode
connection	voltage	tolerance	connection

4. A broadband thermal-noise power PN is measured with a spectrum analyzer at a resolution bandwidth B=1MHz and video filter BV=1kHz. What video filter BV'=? is required for a 10-fold decrease of the measurement uncertainty ΔPN?

(A) 10Hz	(B) 100Hz	(C) 300Hz	(D) 10kHz

5. A high-gain GS>>1 satellite receiver is connected to a noise source with an ENR=5dB and cold temperature T1=T0=290K equal to room temperature. The measured hot/cold ratio equals to Y=4dB. What is the noise temperature TS=? of the receiver?

(A) 75K	(B) 125K	(C) 189K	(D) 290K

6. A DVB-T transmitter uses QPSK-OFDM with N=1705 sub-carriers. What is the theoretical peak output power PMAX=? if the transmitter is required to produce an average RF output power <P>=400W?

(A) 235mW	(B) 400W	(C) 16.5kW	(D) 682kW

7. Our transmitter fTX=168MHz is causing interference to our receiver fRX=158MHz only if both are connected through a frequency duplexer to a common antenna on the tower.
What additional transmitters are suspected to cause PIM (passive IMD) on the tower?

(A) 89MHz & 99MHz	(B) 99MHz only	(C) 99MHz & 148MHz	(D) 148MHz only

8. The output stage of a WiFi OFDM transmitter achieves an efficiency of η=3% at an average output power of <P>=200mW. What 1dB compression point P1dB=? is expected if the power amplifier operates in class A?

(A) +13dBm	(B) +23dBm	(C) +33dBm	(D) +43dBm

9. A two-stage amplifier includes three identical building blocks with Ge=10dB and PPI3e=100W. The driver stage uses one building block while the final stage uses two blocks in parallel. What is the overall PIP3=? if the impedance matching is loss-less?

(A) 100W	(B) 167W	(C) 200W	(D) 333W

10. A Doherty power amplifier includes two similar power amplifiers and two quarter-wave delay lines on the input and output. The two power amplifiers differ in their bias, where the Doherty circuit requires operation in the following classes:

(A) A & B	(A) B & dual B	(C) B & C	(D) A & C

11. A microwave isolator includes a circulator with the third port terminated into a matched load. An ideal microwave isolator has the following S parameters:

(A) |S12|=|S21|=1	(B) |S11|=|S22|=1	(B) |S11|=1 &	(B) |S21|=1 &
& S21=S22=0	& S12=S21=0	S12=S21=S22=0	S11=S12=S22=0

12. A frequency band-pass filter includes a single cavity resonator with a loaded QL=300 at a central frequency of f=2GHz. What is the maximum group delay tg=? of such a band-pass filter?

(A) 48ns	(B) 24ns	(C) 12ns	(D) 6ns

Name:	Email: